## Slide 1
drone-follow → robot-follow
v1.1 design review
From a drone-only app to a robot-generic follow platform.
Branch
feature/rover-support
• 2026-05-13
1

## Slide 2
The talk in one diagram
TODAY v1.1
Camera ─► Hailo ─► Track ─► ReID ─┐ Camera ─► Hailo ─► Track ─► ReID ─┐
▼ ▼
follow_api/controller follow_api/controller
│ │
▼ ▼
VelocityCommand RobotCommand
│ │
▼ ▼
MAVSDK ─► PX4 ─► drone ┌──── Robot protocol ────┐
│ │
▼ ▼
MavsdkDroneAdapter Ros2RoverAdapter
│ │
▼ ▼
PX4 ─► drone rclpy ─► /cmd_vel
─► Gazebo rover
Pipeline / controller / ReID / web UI: unchanged. Only the actuator boundary moves.
2

## Slide 3
Hardware (what runs in the field)
Compute: Raspberry Pi 5 (8 GB) + Hailo-8L M.2
Camera: IMX219 / IMX708 CSI, or USB webcam (dev)
Flight controller: Cube Orange+ via USB serial @ 57 600 baud
Radio: OpenHD WFB over TP-Link USB WiFi (
wlan1
)
Ground: 2nd RPi5 + QOpenHD, or phone
Dev: built-in WiFi (
wlan0
) for SSH, simultaneous with WFB
3

## Slide 4
The job, in five layers
┌──────────────────────────────────────────────────────────┐
│ 1. Camera frames @ 30 fps (CSI / USB / UDP / SHM) │
└─────────────────────────┬─────────────────────────────────┘
│ GStreamer
┌─────────────────────────▼─────────────────────────────────┐
│ 2. Hailo person detection (tiled → unified bboxes) │
└─────────────────────────┬─────────────────────────────────┘
│ HailoDetection
┌─────────────────────────▼─────────────────────────────────┐
│ 3. ByteTracker + ReID gallery / drift / raw fallback │
└─────────────────────────┬─────────────────────────────────┘
│ Detection(cx, cy, bbox_h)
┌─────────────────────────▼─────────────────────────────────┐
│ 4. follow_api/controller yaw + forward + alt + safety │
└─────────────────────────┬─────────────────────────────────┘
│ VelocityCommand
┌─────────────────────────▼─────────────────────────────────┐
│ 5. Actuator: MAVSDK ► PX4 (v1.1: also rclpy ► /cmd_vel) │
└───────────────────────────────────────────────────────────┘
4

## Slide 5
Drone vs rover — capability matrix
Capability
Drone (today)
Rover (v1.1)
Offboard handshake
required (PX4)
none
Arm / takeoff / land
optional
n/a
Altitude control
active P loop
n/a
Yaw units
deg/s (PX4)
rad/s (
Twist
)
Wire protocol
MAVLink via MAVSDK
ROS 2
Twist
Actuator stack
mavsdk_server subprocess
rclpy + executor thread
Bottom-edge safety policy
retreat (tilt headroom)
slow / stop
Yaw-spin search on loss
allowed
typically denied
→
Capabilities
dataclass +
Robot
protocol formalise this.
5

## Slide 6
Codebase today
drone_follow/
├── drone_follow_app.py ◄── composition root + CLI
├── follow_api/ ◄── pure domain (stdlib only)
│ ├── types.py VelocityCommand, Detection
│ ├── state.py SharedDetectionState, FollowTargetState
│ ├── config.py ControllerConfig
│ └── controller.py compute_velocity_command
├── drone_api/ ◄── MAVSDK
│ └── mavsdk_drone.py
├── pipeline_adapter/ ◄── Hailo + GStreamer + tracker + ReID
│ ├── hailo_drone_detection_manager.py (callback hot path)
│ ├── vision_branches.py (display / record / openhd / webui)
│ ├── reid_manager.py
│ ├── byte_tracker.py / fast_tracker.py / tracker_factory.py
├── servers/ ◄── follow + web (MJPEG) + openhd_bridge
├── ui/ ◄── Vite 8 / Node 20
└── tests/
6

## Slide 7
Threading model
GStreamer C lib (Hailo callback) Main thread (asyncio)
───────────────────────────────── ─────────────────────────────────
detection_callback(persons) live_control_loop @ ~30 Hz
│ │
│ ByteTracker.update(persons) │ read latest detection
│ ReIDManager.update_gallery │ compute_velocity_command
│ shared_state.update(detection) │ VelocityCommandAPI.send
▼ ▼
SharedDetectionState ◄── lock ────► MAVSDK offboard stream
(telemetry tasks cache alt)
FollowServer (HTTP) WebServer (HTTP + SSE + MJPEG) OpenHDBridge (UDP)
───────────────────── ──────────────────────────────── ────────────────────
click-to-follow live tuning, video, status follow_id, bbox msgs,
FollowTargetState SharedDetectionState bitrate feedback
3 worlds: detection writes, control reads, servers expose. All cross-thread state is lock-
guarded.
7

## Slide 8
Boundary types
# follow_api/types.py — no third-party imports
@dataclass
class VelocityCommand:
forward_m_s: float # +ve = forward, body frame
down_m_s: float # +ve = down, NED (drone only)
yawspeed_deg_s: float # +ve = CW looking down
@dataclass
class Detection:
label: str
confidence: float
center_x: float # 0.0 – 1.0
center_y: float # 0.0 – 1.0
bbox_height: float # 0.0 – 1.0
timestamp: float
This file is the contract. Renaming
VelocityCommand
→
RobotCommand
is Phase 3.
8

## Slide 9
Follow modes (state machine)
┌─────────────────────────────────────────┐
│ target_state │
│ │
│ ┌────────┐ click bbox ┌────────┐ │
│ │ │ ───────────► │ │ │
│ │ AUTO │ │ LOCKED │ │
│ │ │ ◄─────────── │ │ │
│ └────────┘ reid timeout └────────┘ │
│ ▲ │ ▲ │ │
│ │ │ ground: │ │ │
│ │ │ follow_id=-1 │ │ │
│ │ ▼ │ ▼ │
│ │ ┌────────┐ │ pause │
│ └─┤ IDLE │ ◄─────────────┘ │
│ └────────┘ │
└─────────────────────────────────────────┘
Mode
target_id
paused
explicit_lock
9

## Slide 10
Controller — yaw + forward
┌────────────────────────────────┐ ┌────────────────────────────────┐
│ YAW (always on) │ │ FORWARD (--no-yaw-only) │
│ │ │ │
│ error = cx - 0.5 │ │ factor = target_bbox/bbox −1 │
│ │ │ │
│ yawspeed │ │ forward │
│ ▲ ┌─signed sqrt │ │ ▲ ┌── kp_distance │
│ │ / │ │ │ / (approach) │
│ ───┼──/───► error │ │ ───┼──/────► factor │
│ │ / │ │ │/ │
│ dead│ │ │ dead│ ┌── kp_distance_back │
│ zone│ │ │ zone│ / (retreat — steeper) │
│ │ │ │
│ deg/s, clamped to │ │ m/s, clamped, then │
│ ±max_yawspeed │ │ EMA + slew-rate cap │
└────────────────────────────────┘ └────────────────────────────────┘
Asymmetric retreat gain — no rangefinder, the only safety margin is bbox-size vs panic
threshold.
10

## Slide 11
Controller — altitude + frame-edge safety
┌────────────────────────────────┐ ┌─────────────────────────────────┐
│ ALTITUDE (drone only) │ │ FRAME-EDGE SAFETY │
│ │ │ │
│ err = current - target_alt │ │ ┌──────────────────────────┐ │
│ down = kp_alt * err │ │ │ push (force away) │ │
│ clamp(±max_climb/down) │ │ │═══════════════════════ ═ │margin
│ │ │ │ fade (natural→0) │ │
│ Reads: drone.telemetry. │ │ │═══════════════════════ ═ │ │
│ position() cache │ │ │ │ │
│ │ │ │ (controller zone) │ │
│ v1.1: capability-gated; │ │ │ │ │
│ rover ignores entirely. │ │ │═══════════════════════ ═ │ │
│ │ │ │ fade │ │
│ │ │ │═══════════════════════ ═ │margin
│ │ │ │ push │ │
│ │ │ └──────────────────────────┘ │
│ │ │ │
│ │ │ Top → forward, Bottom → back │
│ │ │ (drone). Rover: bottom = stop. │
└────────────────────────────────┘ └─────────────────────────────────┘
11

## Slide 12
Detection callback (hot path)
per frame (≈ 30 fps, on GStreamer streaming thread)
────────────────────────────────────────────────────
persons : list[HailoDetection] ← Hailo + tile cropper
│
▼
tracker.update(persons) ──► list[TrackedDetection]
│
▼
┌─────────────────────────────────────────────┐
│ choose target: │
│ LOCKED → find by track_id │
│
↳
miss → ReIDManager.try_reidentify │
│
↳
miss → score_visible_persons (RAW) │
│ AUTO → largest_by_bbox │
└─────────────────────────────────────────────┘
│
▼
ReIDManager.update_gallery(target) ◄── drift / dup gates
│
▼
shared_state.update(detection, available_ids)
│
▼
vision_branches pad probe:
• strip tile rectangles
• retag target's HailoDetection → class_id 99
(overlay YAML draws it bigger/greener)
12

## Slide 13
ReID — three similarity bands
sim vs gallery
0.0 ─────────────────────────────────────────────────── 1.0
│ DRIFT │ NORMAL │ DUPLICATE │
│ sim < 0.6 │ 0.6 ≤ s ≤ 0.9│ sim > 0.9 │
│ │ │ │
│ → don't │ → store │ → skip │
│ store │ FIFO-out │ → every Nth dup: │
│ → run │ oldest │ refresh oldest │
│ re-acquire│ │ │
│ pass │ │ │
Plus raw-detection fallback: if tracker emits zero tracks but raw
persons
exist, score
them directly. Locked-follow survives tracker dropouts.
Knobs:
--reid-threshold 0.75
,
--reid-drift-threshold 0.6
,
--reid-
duplicate-threshold 0.9
,
--reid-refresh-every 5
,
--reid-timeout 20.0
,
--
update-interval 10
.
13

## Slide 14
Vision branches (output tree)
source ─► tile_cropper ─► user_callback ─►┐
│ output_tee
┌─────────────────────────────────────┼─────────────────────────┐
▼ ▼ ▼
[--webui] [--openhd] [--display / --record]
MJPEG appsink RTP/UDP H.264 retag target class_id=99
(client renders to OpenHD ground ↓
bboxes from JSON) hailooverlay_community
(show-tiles=false, YAML)
↓ local_tee
┌──────┴──────┐
▼ ▼
[--display] [--record]
fpsdisplaysink valve+x264+mkv
--webui
and
--openhd
are mutually exclusive (single network encoder).
Implicit-display rule: if neither UI flag is set,
--display
defaults on.
No HW H.264 on RPi5 → x264 software encode for both.
14

## Slide 15
MAVSDK adapter + servers
drone_api/mavsdk_drone.py
— only place that imports
mavsdk
.
VelocityCommand ──► VelocityCommandAPI.send ──► drone.offboard.set_velocity_body
(clamp ► EMA ► slew cap) (VelocityBodyYawspeed)
detached mavsdk_server ◄── subprocess ──► PX4 over UDP / serial
(survives Ctrl+C → graceful land)
Lifecycle (when
--takeoff-landing
set): arm → takeoff → setpoint loop → land.
Otherwise: stream zeros, wait for pilot OFFBOARD switch. Offboard-loss watchdog
never auto-switches modes.
Three servers (all run in their own threads):
Server
Port
Surface
FollowServer
8080
HTTP click-to-follow / target API
bS
00
i
G
SS
li
d
i
15

## Slide 16
CLI & configuration
Pipeline: --input {rpi|usb|udp://…|shm://…}, --input-codec, --tiles-x/y
Drone: --connection, --serial, --takeoff-landing, --target-altitude,
--target-bbox-height, --yaw-only / --no-yaw-only
ReID: --reid-* (8 flags) Tracker: --tracker {byte|fast}
UI: --webui / --openhd / --display / --record (mutex rules apply)
Controller: every numeric ControllerConfig field (also live-tunable)
Config layering (lowest → highest priority):
ControllerConfig dataclass defaults
│
▼
JSON file via --config
│ (configs/simulation.json, simulation_follow.json, df_params.json)
▼
CLI flags (--kp-yaw=…, --max-forward=…)
│
▼
Live UI sliders (web UI + OpenHD bridge)
16

## Slide 17
Run-time scenarios
Dev: USB cam + real Cube Sim: PX4 SITL + Gazebo
┌──────┐ USB ┌─────────────┐ gz sim ──gz-transport──► video_bridge.py
│laptop│◄────────│ drone-follow│ │
│ +Cube│ serial │ --input usb │ UDP 5600 ◄─┘ ► drone-follow
│ Or+ │◄────────│ --serial │ ┌─UDP 14540────► PX4 SITL ◄─MAVSDK──┘
└──────┘ │ --webui │
└─────────────┘
Real flight, Mode A (drone-follow owns CSI cam)
CSI ─► drone-follow ─► overlay+x264 ─► OpenHD air ─► WFB ─► OpenHD gnd ─► QOpenHD
(--input rpi --openhd)
Real flight, Mode B (OpenHD owns CSI cam, tees SHM)
CSI ─► OpenHD ─tee─► /tmp/openhd_raw_video ─► drone-follow (AI only)
└──► WFB ─► QOpenHD
scripts/start_air.sh --mode {stream|shm}
selects mode;
install_air.sh
must
match.
17

## Slide 18
Boot service (field deployment contract)
systemd
│
▼
/etc/systemd/system/drone-follow-boot.service ◄── name preserved (RENAME-04)
│
▼
scripts/boot/drone-follow-boot.sh
│
▼
~/Desktop/drone-follow.conf ENABLED=true ◄── operator-editable
│ MODE=stream|shm
▼
scripts/start_air.sh [--mode …]
│
▼
drone-follow --input rpi --openhd --connection tcpout://127.0.0.1:5760 …
Three Pis in the field share this contract. Breaking it = breaking the fleet.
18

## Slide 19
Part 2 — v1.1 changes
What
feature/rover-support
ships.
19

## Slide 20
Where the drone-only assumption leaks (11 sites)
Where
Leak
Fix
drone_follow_app.py
run_drone()
,
drone args always
run_robot()
, dispatch on
--ro
follow_api/types.py
VelocityCommand
,
down_m_s
RobotCommand
; altitude optional
follow_api/controller.py
altitude P
unconditional
gate on
has_altitude
follow_api/controller.py
bottom-edge =
retreat-from-tilt
capability-gate, rover = slow/stop
follow_api/controller.py
yaw-spin on loss
assumed allowed
capability flag
20

## Slide 21
The 6 phases
Phase 1 ── Rename Phase 2 ── Cleanup
drone_follow → robot_follow Dead code, dups, hot-path races
(mechanical) (CLEAN-01..18)
│ │
└─────────────►◄───────────────────┘
│
▼
╔═══════════════════════════════════════════╗
║ Phase 3 ── Robot protocol + Capabilities ║
║ MavsdkDroneAdapter; --robot flag ║
║ CRITICAL GATE ║
║ drone SITL must pass end-to-end here ║
╚════════════════════╤══════════════════════╝
│
┌───────────┴───────────┐
▼ ▼
Phase 4 ── Rover adapter Phase 5 ── Rover sim
rclpy + Twist + cmd_vel Gazebo Garden SDF +
SIGINT-safe thread cmd_vel bridge +
video_bridge.py reuse
│ │
└───────────┬───────────┘
▼
Phase 6 ── Sim integration
rover-safe defaults, bottom-edge repurpose,
ByteTracker config, end-to-end test
21

## Slide 22
Phase 1 — Rename
Goal:
pip show robot_follow
works,
pip show drone_follow
returns nothing. Both
drone-follow --help
and
robot-follow --help
produce identical output. Boot
service unit file unchanged on disk.
git mv drone_follow robot_follow ◄── single atomic commit
│
├─ 48 internal imports rewritten
├─ drone_follow_app.py → robot_follow_app.py
├─ pyproject.toml: name = "robot-follow"
│ scripts: robot-follow + drone-follow (alias)
├─ install.sh: pip uninstall drone-follow -y (defensive)
├─ shell scripts: setup_env.sh / install_air.sh / start_air.sh
├─ docs: every example rewritten; one alias note
│ in README + CLAUDE.md
└─ git grep gate: drone_follow|from drone_follow|import drone_follow
→ only docs/history whitelist matches
Stays put:
drone_api/
subdir (renames in Phase 3),
ui/
,
recordings/
, boot unit
file
~/Desktop/drone-follow conf
Branch scope: lives only on
feature/rover-
22

## Slide 23
Phase 2 — Cleanup (18 items, three buckets)
Dead code (10)
Duplication (5)
Hot-path (3)
world_loader.py
mavsdk_server pkill
helper
CLEAN-16 SSE race
(next slide)
bench_reid_callback
3× argparse pre-parsers
→ 1
CLEAN-17 socket-per-
call → reuse
--vfov
telemetry position+alt
tasks
CLEAN-18 O(n) dedup →
O(1) dict
--mission-duration
tunable_fields()
unification
serial_baud=115200 fallback
branch-decision tree
unified
23

## Slide 24
Phase 2 — CLEAN-16 (SSE race)
BEFORE (web_server.py:84) AFTER
───────────────────────────── ──────────────────────────────
def _on_frame(...): def _on_frame(...):
self._frame_event.set() with self._cond:
self._frame_event.clear() self._frame_seq += 1
self._cond.notify_all()
def _sse_handler(): def _sse_handler():
self._frame_event.wait(timeout=2.0) last = -1
# race: clear() may fire while True:
# between set() and second with self._cond:
# consumer's wait() self._cond.wait_for(
# → consumer falls through lambda: self._frame_seq != last,
# 2 s timeout timeout=2.0)
last = self._frame_seq
Two browser tabs watching the MJPEG — today, one stalls. Tomorrow, both update on
every frame.
24

## Slide 25
Phase 3 — Robot protocol + Capabilities
@dataclass(frozen=True)
class Capabilities:
has_altitude: bool
needs_offboard_handshake: bool
needs_takeoff_landing: bool
yaw_units: Literal["deg/s", "rad/s"]
@dataclass
class RobotCommand: # replaces VelocityCommand
forward: float # m/s
yaw: float # in `yaw_units`
altitude: float = 0.0 # m, ignored when has_altitude=False
class Robot(Protocol):
capabilities: Capabilities
async def connect(self) -> None: ...
async def start_session(self) -> None: ...
async def send_command(self, cmd: RobotCommand) -> None: ...
async def send_zero(self) -> None: ...
async def shutdown(self) -> None: ...
25

## Slide 26
Phase 3 — live_control_loop capability gates
┌──────────────────────────────────────────────────────────────┐
│ compute_velocity_command(detection, config) │
│ │ │
│ ▼ │
│ base RobotCommand(forward, yaw) │
│ │ │
│ ├─ if caps.has_altitude: │
│ │ cmd.altitude = altitude_p_loop(curr, target) │
│ │ │
│ ├─ if caps.has_altitude: │
│ │ drone_bottom_edge_retreat(cmd, det) │
│ │ else: │
│ │ rover_bottom_edge_slowstop(cmd, det) │
│ │ │
│ └─ if caps.can_yaw_spin_to_search: │
│ yaw_spin_search(cmd) │
│ │
└──────────────────────────────────────────────────────────────┘
│
▼
robot.send_command(cmd)
26

## Slide 27
Phase 3 —
--robot
two-pass argparse
PASS 1 PASS 2 (conditional)
────────── ─────────────────────────
pre.add_argument("--robot", parser = build_common()
choices=["drone","rover"], if pre_args.robot == "drone":
default="drone") add_drone_args(parser)
pre_args, _ = pre.parse_known() else:
add_rover_args(parser)
args = parser.parse_args()
--robot drone --help
shows
--takeoff-landing
,
--target-altitude
,
--
serial
--robot rover --help
shows
--cmd-vel-topic
,
--ros-namespace
,
--ros-
domain-id
Folds into the existing pre-parse stack (output flags, ReID, tracker) — CLEAN-12
collapses all of those into one stage.
27

## Slide 28
Phase 4 — rover adapter (rclpy on a thread)
┌───────────────────────────────────────────────────────────────┐
│ Main thread (asyncio) │
│ live_control_loop ──► robot.send_command(cmd) │
│ │ │
│ ▼ │
│ publisher.publish(Twist) │
│ (thread-safe — rcl lock-protected) │
│ │ │
├──────────────────────────────┼────────────────────────────────┤
│ rclpy-spin thread │ (background, daemon) │
│ while not shutdown: │ │
│ executor.spin_once(0.05) │ │
│ │ │
│ ▼ │
│ Twist on /cmd_vel ───► ROS / gz bridge │
└───────────────────────────────────────────────────────────────┘
rclpy.init(signal_handler_options=SignalHandlerOptions.NO) # ← non-negotiable
node = Node("robot follow rover")
28

## Slide 29
Phase 4 — the SIGINT trap
┌─────────────────────────────────────────────────────────────────┐
│ default rclpy.init() │
│ │
│ installs rclpy's SIGINT handler ──► silently overrides │
│ drone-follow's on_signal │
│ │
│ Ctrl+C → rclpy says "shutting down" │
│ → publisher stops │
│ → BUT: no zero-velocity command sent │
│ → rover keeps moving on last Twist │
└─────────────────────────────────────────────────────────────────┘
┌─────────────────────────────────────────────────────────────────┐
│ rclpy.init(signal_handler_options=SignalHandlerOptions.NO) │
│ │
│ drone-follow's on_signal stays installed │
│ Ctrl+C → on_signal → send_zero() → shutdown() → rover stops │
└─────────────────────────────────────────────────────────────────┘
29

## Slide 30
Phase 5 — rover sim (one command)
start_rover_sim.sh
│
├─► gz sim sim/rover/worlds/walk_across_then_approach.sdf
│ │
│ ▼
│ rover.sdf: <plugin filename="gz-sim-diff-drive-system"
│ name="gz::sim::systems::DiffDrive">
│ <topic>cmd_vel</topic> ◄── override default
│ </plugin>
│ + camera sensor
│
├─► ros2 run ros_gz_bridge parameter_bridge \
│ /cmd_vel@geometry_msgs/msg/Twist@gz.msgs.Twist
│
└─► python sim/bridge/video_bridge.py \
--topic /model/rover/sensor/camera/image \
--host 127.0.0.1 --port 5600 ◄── EXISTING tool, reused
drone-follow runs unchanged:
robot-follow --robot rover --input
udp://0 0 0 0:5600
30

## Slide 31
Phase 5 — Garden gotchas (all silent failures)
Field
WRONG (Ignition era)
RIGHT (Garden era)
SDF
plugin
filename
libignition-gazebo-diff-drive-
system.so
gz-sim-diff-drive-system
SDF
plugin
name
ignition::gazebo::systems::DiffDrive
gz::sim::systems::DiffDriv
Bridge
msg
type
…@ignition.msgs.Twist
…@gz.msgs.Twist
Apt
bridge
ros-humble-ros-gz-bridge
(Fortress)
ros-humble-ros-gzgarden-
31

## Slide 32
Phase 6 — rover-safe defaults + bottom-edge repurpose
configs/rover_simulation.json
─────────────────────────────
{
"max_forward": 1.0, (was 4.0 for drone)
"max_backward": 0.5,
"kp_yaw": 60, (was 120 — narrower yaw dynamics)
"kp_distance": 1.0,
"_omitted": "all altitude knobs — capability-gated off",
"tracker": {
"track_thresh": 0.4,
"track_buffer": 30, (was 90 → 1 s vs 3 s @ 30 fps)
"match_thresh": 0.8
}
}
bottom-edge safety
───────────────────────────────────────────────────────────────
if caps.has_altitude: if not caps.has_altitude:
# DRONE: retreat for tilt
# ROVER: slow / stop
32

## Slide 33
Phase 6 — end-to-end test (RINT-04 + RINT-06)
test_rover_follow_walk_across_then_approach
────────────────────────────────────────────
start sim (walk_across_then_approach world)
│
▼
launch robot-follow --robot rover --config rover_simulation.json
│
▼
wait for first detection ◄── timeout 10 s
│
▼
capture target_id
│
▼
run 45 s
│
▼
ASSERT target_id_lost_events == 0
ASSERT final_target_id == initial_target_id
│
▼
Ctrl+C
│
▼
ASSERT /cmd_vel messages within 100 ms == 0 ◄── RINT-06
ASSERT rover stopped within 1 s
33

## Slide 34
Before / after architecture
TODAY v1.1
drone_follow_app.py robot_follow_app.py
│ │
│ │ pre-parse --robot
▼ ▼
run_drone() run_robot(args)
│ │
▼ ├─► MavsdkDroneAdapter
follow_api / pipeline_adapter │ (moved from drone_api/
│ (unchanged) │ to robot_api/adapters/)
▼ │
VelocityCommand └─► Ros2RoverAdapter ◄── NEW
│ │ rclpy + Twist
▼ │ on /cmd_vel
drone_api.mavsdk_drone [capability-gated controller]
│ │
▼ ▼
PX4 ─► drone PX4 │ Gazebo rover
│
NEW: │
robot_api/robot.py
robot_api/adapters/ros2_rover.py
sim/rover/
configs/rover_simulation.json
34

## Slide 35
Risks (ranked)
#
Risk
Severity
Mitigation
1
rclpy steals SIGINT → rover
keeps moving on Ctrl+C
HIGH
SignalHandlerOptions.NO
; post-init
assert; RINT-06 test
2
Phase 3 regression breaks
drone SITL
HIGH
Critical gate — full SITL test must
pass before Phase 4/5
3
_rclpy_pybind11
ImportError in hailo venv
MEDIUM
Defensive import;
setup_env.sh
auto-sources ROS
4
Garden silent SDF load
failure (
ignition::
prefix)
MEDIUM
PITFALLS.md + README;
gz
topic -l
validation step
5
ros_gz_bridge
15 Hz
camera ceiling
MEDIUM
Avoid: reuse
video_bridge.py
(gz-
transport)
35

## Slide 36
Out of scope (v1.1)
Excluded
Reason
Real rover hardware
Sim can't validate HW safety → v1.2
Nav2 / ros2_control
Goal-based pathing, wrong message types
SLAM / mapping
Requires LiDAR / depth — not on BoM
Non-Humble ROS 2
distros
Iron EOL Dec 2024; Jazzy has no Jammy binaries
Gazebo Harmonic
migration
Garden EOL but SDF is already
gz::
-compatible
Multi-robot fleet control
Single-target controller is the validated abstraction
Mid-run robot-type
switching
Requires pipeline restart
36

## Slide 37
Where we are now / next
feature/rover-support (5 commits ahead of main, all docs)
─────────────────────────────────────────────────────────────
.planning/PROJECT.md
.planning/REQUIREMENTS.md 55 numbered reqs
.planning/ROADMAP.md 6 phases
.planning/research/ stack / features / arch / pitfalls
.planning/phases/01-rename/01-CONTEXT.md ◄── decisions locked
.planning/presentations/v1_1_overview.md ◄── this deck
▼
/gsd:plan-phase 1
▼
.planning/phases/01-rename/01-PLAN.md
▼
/gsd:execute-phase 1
▼
atomic rename commit
Questions / pushback / "we should also…" → now is the moment.
37